## Slide 1
BIOREMEDIATION
GROUP MEMBERS
ADITYA PHUKAN(20802002)
HARSHIT BORA(20802003)
PRIYANSHU GUPTA(20802011)
NIRMAN BATRA(20802014)

## Slide 2: Definitions
Bioremediation is a branch of biotechnology that employs the use of living organisms, like microbes and bacteria, in the removal of contaminants, pollutants, and toxins from soil, water, and other environments.
Bioremediation is used to clean up oil spills or contaminated groundwater.
Bioremediation may be done "in situ"–at the site of the contamination–or "ex situ"–away from the site.
Bioremediation uses biological agents, mainly microorganisms i.e. yeast, fungi or bacteria to clean up contaminated soil and water.
This technology relies on promoting the growth of specific micro flora or microbial consortia that are indigenous to the contaminated sites that are able to perform desired activities

## Slide 3
Bioremediation is a triple-corners process:
Organisms
Pollutants
Environments
Microorganisms
Plants
Enzymes
Soil
Water
Air
Organic
Inorganic
Solid
Liquid
Gas

## Slide 4: Bioremediation related topics
Biosurfactants
Bioremediation techniques
Environments
Organisms
Phytoremediation
Bioremediation of metals polluted environment
Enzymes separation and identification
Cells immobilization
Pollutants
Bioremediation
Enzymes immobilization

## Slide 5: Stages of a biodegradation study
1- Isolation of the microorganism
5- Determination of the biodegradation efficiency
4- Optimization of the biodegradation conditions
3- Identification of the microbial isolate
2- Purification of the obtained isolates
6- Identification of the biodegradation products.
7- Cell or enzyme immobilization.
8- Enzyme identification.

## Slide 6: Cells and Enzymes immobilization:
Immobilized enzymes (or cells) is defined as the enzyme that physically or chemically confined in defined materials with retention of its catalytic activity.
The immobilization methods
1- Carrier-binding methods.
2- Cross-linking methods.
3- Entrapping methods.
1) Covalent binding methods
2- Ionic binding methods.
3- Physical adsorption.
4- Bio-specific binding methods.
3- Membrane.
2- Microcapsule.
1- lattice method.
4- Reversed micelle.

## Slide 7: Materials used in the Carrier-binding methods
1- Polysaccharides: cellulose, dextran and agarose derivatives.
2- Proteins: gelatin, albumin.
3- Synthetic polymers: Polystyrene derivatives, ion exchange resins, polyurethane.
4- Inorganic materials: glass, sand, ceramic and magnetite.

## Slide 8
1) Covalent binding methods include:
a) Cyanogen Bromide method (CNBr).
b) Acid-azide derivative method
c) Condensing reagent methods
d) Diazo coupling methods
e) Alkylation methods.
Figure1: Steps of CNBr enzyme immobilization method

## Slide 9: B- Cross-linking methods:
By cross-linking of the enzyme molecules by reacting with glutaraldehyde.
A cross-link is a bond that links one polymer chain to another.

## Slide 10: 3- Materials used in the entrapping methods
a) Lattice type:
polyacrylamide,
calcium algenate,
polyvinylalcohol polymers.
b) Microcapsule type:
Interfacial Polymerization Method.
Liquid drying method.

## Slide 11: Phytoremediation
Phytoremediation is use of plants for accumulation, removal or conversion of pollutants.
Phytoremediation
Phytostabilization
Phytotransformation
Phytoextraction
Phytovolatilization
Phytostimulation

## Slide 13
Approximately 400 plant species have been classified as hyperaccumulators of heavy metals, such as grasses, sunflower, corn, hemp, flax, alfalfa, tobacco, willow, Indian mustard, poplar, water hyacinth, etc.

## Slide 14
The root exudates of these plants play an important role in phytoremediation as it activate the surrounded microorganisms.
Genetic engineering are used as in case of BT protein or insect pheromones producing plants to reduce the use of pesticides.

## Slide 15
Metals bioremediation mechanisms
Solubilization
(Bioleaching)
Complexation
(Bioaccomulation)
(Biosorption)
Metal immobilization
Precipitation
- H2S producing bacteria
- Siderophores.
- Metal reduction.
- Exopolysaccharide.
- Lipoproteins.
- Organic acids.
- Siderophores.
- Root exudates.

## Slide 16: Contaminants Potentially Amenable to Bioremediation ____________________________________________

## Slide 17
The biosurfactants are chemical compounds characterized by hydrophobic and hydrophilic (non-polar and polar) regions in one molecule (amphipathic molecules).
Biosurfactants from bacteria, cyanobacteria, fungi and yeast are classified into:
Glycolipids.
Lipopeptides.
Phospholipids.
Glycoproteins.
Polymeric biosurfactants.
Biosurfactants
Notes: 17

## Slide 18: Physiological roles of biosurfactants:
1- Increase the availability of hydrophobic compounds
2- Nutrient storage molecules.
3- Save the microbial cells from toxic substances.
4- Efflux of harmful compounds.
5- Extracellular and intracellular interactions such as quorum sensing and biofilm.

## Slide 19: Biosurfactant applications in bioremediation:
The microbe may access a poorly water-soluble substrate that has been “pseudosolubilized” by the biosurfactant.
Reduce the adsorption of the non-polar pollutants to the surface of soil particles.

## Slide 20: Bioremediation techniques:
(1) In-situ (without excavation).
(2) Ex-situ (with excavation).
Only ex-situ processes allow an efficient optimization of incubation parameters (biostimulation), including:
pH,
Aeration,
Agitation,
Moistening
nutrients,
solvents or surfactants.
In addition to addition of microorganisms (bioaugmentation).

## Slide 21
The ex-situ technique includes:
1- Bioslurry reactor.
2- Biopile.
3- landfarming
Bioslurry reactor.
Biopile.
Biopile.

## Slide 22
FIELD WORK

## Slide 23
FIELD WORK

## Slide 24
Bioremediation provides a technique for cleaning up pollution by enhancing the natural biodegradation processes. So by developing an understanding of microbial communities and their response to the natural environment and pollutants, expanding the knowledge of the genetics of the microbes to increase capabilities to degrade pollutants, conducting field trials of new bioremediation techniques which are cost effective, and dedicating sites which are set aside for long term research purpose, these opportunities offer potential for significant advances. There is no doubt that bioremediation is in the process of paving a way to greener pastures. Regardless of which aspect of bioremediation that is used, this technology offers an efficient and cost effective way to treat contaminated ground water and soil. Its advantages generally outweigh the disadvantages, which is evident by the number of sites that choose to use this technology and its increasing popularity. Once again thanks to the bioremediation technology to clean up the polluted environment and therefore may be used as management tool.